WORKING IN THE CHEMISTRY LABORATORY

I.	THE LAB BURNER

Materials:	Burner		Copper wire		Paper Clip

Striker		Aluminum wire		Crucible tongs

Match		Iron wire		Test tube holder

Paper clip				Small test tube

1.	Most laboratory burners are constructed in a similar fashion.  There is an inlet for the gas, an adjustment for the amount of gas, and an adjustment for the amount of air.  (See diagram).  A proper mix of air and gas will yield a faint blue flame for maximum heat and minimum soot.

2.	Examine your burner before you try to light it.

Identify the gas adjustment and air adjustment.  Close

the air vents and connect the burner to the source of gas.

Turn on the gas just enough so that it can be barely heard.

Hold the striker above the barrel of the burner and produce

a spark from the striker to start the flame.

3.	Hold the empty dry test tube with the test tube holders and

put it into the flame until you notice a change on the

test tube.  Set the test tube on the bench top to cool.  When

cool, examine the outside of the test tube.  (use a good flame and bad flame, note observations)

Q #1:  Using complete sentences, describe the flame when the air vents are closed.  Describe what happened to the test tube.  Suggest a reason for this observation.

4.	Adjust the flame to a blue color, about 1-1/2 to 2 inches tall, without a roaring sound, by changing the amount of air and the amount of gas.  Adjust the flame so that there is an inner cone (see diagram below).

You should be able to identify three regions in

the burner flame as shown in the accompanying figure.

Q #2: Sketch the burner flame as it looks with the air vents open.  Label the regions A, B, and C on your flame.  Indicate the color(s) present in the flame.

5.	The temperature of the flame in its various regions will be determined by placing metal

wires into the flame and seeing if they melt, NOT THERMOMETER.  The wires to be used are:

Aluminum:	melting temperature = 660 o Celsius

Copper:	melting temperature =1080o Celsius

Iron:		melting temperature = 1540oCelsius

Make a small loop on the end of the aluminum wire.  Holding the wire with tongs, place the loop in each of the regions of the flame, starting at the bottom of the flame and slowly raising the loop through the flame, in order the identify the region(s) in which each wire melts.

Repeat the above procedure using copper wire and then iron wire.

Q #3: Record your observations of these three wires in the flame.

Q #4: Where is the hottest region of the flame?  State an approximate temperature range for this region? (no thermometers in flame)

6.	Turn off the burner at the gas valve on the lab bench.  Push a paper clip half-way

onto a match, slightly below the head of the match.  Place the

wooden end of the match into the barrel of the burner, so that

the paper clip supports the match on the top of the burner.

Light the burner with the striker.

Q #5:  Describe what happens to the match.  What does this suggest to you about the burner flame?

II.	REACTION OF MAGNESIUM WITH HYDROCHLORIC ACID

Materials:	Graduated cylinder (10 mL)		Magnesium strip

Thermometer				Hydrochloric acid (HCl)

Test tube

1.	Pour about 5 mL of hydrochloric acid into a graduated cylinder.  (Be sure to use proper methods of removing a stopper from a reagent bottle and pouring from a reagent bottle.)

Graduated cylinders are designed to read correctly only if the bottom of the meniscus is the point where the volume is recorded.  (A meniscus is the slight curve that appears on the surface of many liquids.)  Read the volume when your eyesight is level with the bottom of the meniscus.

2.	Pour the acid from the graduated cylinder into the test tube.  Determine the temperature of the acid using the thermometer.   Do not attempt to “shake down” a laboratory thermometer.

Q #6: Record the temperature of the acid, estimating to the nearest tenth of a degree.

3.	Place the piece of magnesium into the acid and observe the reaction.  When the reaction has ceased, again determine the temperature of the contents.

Q #7: What are your observations of the reaction?

Q #8: What is the temperature at the end of the reaction?

Q #9: Reactions that give off heat are called  exothermic, while reactions that absorb heat are called  endothermic.  Was the reaction of magnesium and hydrochloric acid endothermic or exothermic?  Explain your choice.

III.	FILTRATION OF A SAND-SALT-WATER MIXTURE

Materials:	Sand		Tap water		2-250 mL beakers

Salt		Stirring rod		Graduated cylinder, 100 mL

Tongs		Filter paper		Ring and stand

Funnel		Evaporating Dish	Wire gauze

Sometimes liquids contain particles of insoluble solids, either present as impurities or formed by the interaction of chemicals.  If they are more dense than water, they sink to the bottom.  Most of the clear liquid above the solid can be poured off without disturbing the precipitate.  Such a method of separation is known as  decantation.  Fine particles, which settle slowly, are often separated from a liquid by  filtration.  In this section of the lab exercise, you will prepare a salt-sand-water mixture, which will then be filtered.

1.	Into a beaker place a small spatulaful of salt and about an equal amount of sand.  Using a graduated cylinder, measure out about 50 mL of distilled water and pour it into the beaker containing the salt and sand.  Stir the mixture with a stirring rod.

2.	Set up the filtration apparatus as shown in the

diagram.  Fold the filter paper along its diameter, then

fold it again to form quadrants.  Open up the paper so

that it forms a cone.  Place the paper into the funnel.

Moisten the filter paper with a few drops of water							 so that it will stick to the funnel.

3.	Pour the liquid mixture into the filter paper

in the funnel.  Do not overflow the paper.  Try to

establish a water column in the stem of the funnel, 						       thus excluding air bubbles.  Add the liquid just fast

enough to keep the level under the top of the paper.

4.	After you have finished filtering, pour about 1/3

(approx. 10-15 mlof the  filtrate (the liquid that has

passed through thefilter paper) into the evaporating dish.

Place the dish on a wire gauze, atop a ring on the ring stand.

Lower or raise the ring so that the bottom of the wire gauze will be at the hottest part of the flame.  Evaporate the liquid nearly to dryness.  Remove the flame when the solid particles begin to spatter out of the dish.  Remove the hot dish to a second cool wire gauze using tongs.

Q # 10: What property of sand enables it to be separated from the liquid by filtration?

Q #11: What is the substance remaining on the filter paper after the filtration?

Q #12:  What does the filtrate contain?

Q #13: What is the residue left in the evaporating dish after the liquid was evaporated?

Q#14:  What characteristics of salt prevents it from being separated from the water by

filtration?

# Text boxes

Burner tube

Gas control valve

Gas inlet

Air vents

C

B

A